## Slide 1: Non-Ideal Meters
IB Physics | Electricity

## Slide 2
The Observer Effect
When taking any scientific measurement, there is always the possibility that the act of taking the measurement will change what is being measured

## Slide 3
The Observer Effect
When we measure voltage or current in a circuit, we want to make sure to minimize an effect that our tool has on the circuit so that we get the most accurate results
Voltmeter
Ammeter
A
V

## Slide 4
Ammeter
Hooked up in series with the component being measured
Ideal Ammeter:
[R = ]
A
0 Ω

## Slide 5
Measuring the Current
A
What is the reading for the current flowing through this ideal ammeter?
R1
R2
6 Ω
2 Ω
0 Ω
The ammeter has no effect on the current that it’s measuring
12 V

## Slide 6
What if Ammeter isn’t ideal?
A
12 V
R1
R2
6 Ω
2 Ω
0 Ω
The non-ideal ammeter’s resistance slows down the current that it’s measuring
What is the reading for the current flowing through this ideal ammeter?
2 Ω
2 Ω

## Slide 7
Voltmeter
V
Hooked up in parallel with the component being measured
Ideal Voltmeter:
[R = ]
∞ Ω

## Slide 8
Measuring the Voltage
What is the reading for the ideal voltmeter across the resistor R1?
12 V
R2
2 Ω
∞ Ω
V
R1
6 Ω
0

## Slide 9
Measuring the Voltage
What is the reading for the ideal voltmeter across the resistor R1?
12 V
R2
2 Ω
∞ Ω
V
R1
6 Ω
12 Ω
12 Ω

## Slide 10
Try This
A
12 V
Calculate the resistance of this non-ideal meter:
Ammeter Reading | 1.2 A
R1
R2
3 Ω
6.5 Ω
1.2 A
Current is the same for all components
Calculate total resistance from voltage and current
Calculate ammeter resistance

## Slide 11
Try This
V
12 V
Calculate the resistance of this non-ideal meter:
Voltmeter Reading | 7 V
R1
R2
4 Ω
2.5 Ω
Use voltage loops to calculate voltage for R1 and R2
Calculate current for R1 and R2
Use current junction to find current through meter
Calculate resistance of voltmeter
7 V
5 V
1.75 A
2 A
2 A
1.75 A
0.25 A
0.25 A

## Slide 12
Lesson Takeaways
I can connect a meter to measure current or voltage
I can describe the conditions required for an ideal ammeter or voltmeter
I can calculate for a situation when the meter isn’t ideal